2 bits addressing 8 bits registers
SP = 0x0 stackpointer
R1 = 0x1
R2 = 0x2
R3 = 0x3

Extra not directly accessible registers
PC: Program Counter (8 bits)
SR: Status Register (3 bits) [ GREATERBIT EQUALBIT CARRYBIT ]

4 bit instruction opcode, 8 bit instruction size
0x0 cmp RX RY: compares RX with RY, sets equals SR bit if equals, sets greater SR bit if RY > RX
0xa lb RX RY: load byte pointed by RX in RY
0x1 sb RX RY: save byte in RY on RX’s pointing position on memory
0x2 ??
0x3 lui NUM RY: copy on RY 2 bits NUM on LSB
0x4 sla NUM RY: shift left by NUM RY
0x5 sra NUM RY: shift right by NUM RY
0x6 and RX RY: do logical AND on RY using RX as mask
0x7 or RX RY: do logical OR on RY using RX as mask
0x8 add RX RY: adds RX to RY, sets carry bit on SR if carry occurs
0x9 ??
0xb br NUM: jump to PC+NUM[3:0] position
0xc jeq NUM: jump to PC+NUM[3:0] position if equals SR bit is set
0xd jgt NUM: jump to PC+NUM[3:0] position if greater SR bit is set
0xe jc NUM: jump to PC+NUM[3:0] position if carry SR bit is set
0xf j RX: jump to RX position